## Slide 1
AIR Hypervisor using GR740 and N2X
GR740 User Day

## Slide 2: CONTENTS
AIR Overview
MULTIMA
HAIR
NGT-ATB
VERICOCOS
ESROCOS
COMRADE
MORA-TSP
Page 2

## Slide 3
Overview
AIR

## Slide 4
What is AIR
AIR overview
Page 4
AIR is a type-1 hypervisor that guarantees TSP in the target hardware
Allows multiple avionics applications with different criticalities to run independently in the same hardware resource
Development
Integration
Prototyping
REAL-TIME HYPERVISOR
COMPLIANT WITH ARINC 653 and IMA-SP

## Slide 5
AIR supports paravirtualized RTOS versions for SPARC:
RTEMS version 4.8i (a space tailored version of RTEMS 4.8 by Edisoft[1])
RTEMS version 5
  SMP
  Flexibility to move tasks across different schedulers and reassign cores to schedulers
RTEMS
Supported RTOS
Page 5
[1] - “RTEMS by Edisoft” Edisoft - Defense & Aerospace, www.edisoft.pt/product-list/rtems

## Slide 6
MULTIMA
GR740 WITH

## Slide 7
TSP in Multicore
Objectives
Page 7
There is new processor and development board is in town. NGMP – N2X
It is multicore with 4 processors.
AIR goes multicore and let’s benchmark it!

## Slide 8
BENCHMARK RESULTS
MULTIMA 2013
Page 8
Window Slot (s) | Execution Time (s) | Iterations per second | CoreMark[2] | Performance Loss
NO AIR | 12.070 | 166 | 1.105 | -
1.000 | 12.240 | 163 | 1.089 | 1.38%
0.500 | 12.240 | 163 | 1.088 | 1.39%
0.010 | 12.450 | 161 | 1.074 | 2.77%
0.001 | 12.669 | 157 | 1.050 | 4.88%
Amdahl law happened as expected!
AIR presence overhead grows inversely with window size
[2] - “CoreMark® An EEMBC Benchmark”, EEMBC, https://www.eembc.org/coremark/
Chart: Processing time V.S. Number of cores
 | 25.02 | 12.84 | 8.59 | 6.45

## Slide 9
HAIR
GR740 WITH

## Slide 10: EMULATE GR740
OBJECTIVES
Same Functional behaviour of the OBSW
Same time profile of execution OBSW
Same TSIM like interface to user
Same impact of SW running on other cores/partitions
OBSW
OBSW

## Slide 11: HAIR Emulation – Binary Timing Mode
EMULATOR DESCRIPTION
Hairdresser
Execution
Profile DB
OBSW Source
AIR Config.
(XML)
HAIR Configuration
Script File

## Slide 12: Accurate Timing
RESULTS

## Slide 13
NGT-ATB
GR740 WITH

## Slide 14: ATB for Next Generation Launcher
OBJECTIVES
Implementation of a ADR use case running at ESTEC ATB with GR740

## Slide 15: Active Debris Removal Use
USE CASE
GR740 provide enough computation power for a complex GNC algorithm

## Slide 16: Integration with all Testbed tools
RESULTS
Binary image created with Matlab and TASTE.
Execution in full SVF/AIV environment.

## Slide 17
VERI
COCOS
GR740 WITH

## Slide 18: VERICOCOS Toolchain
OBJECTIVES
AAML Editor
OSRA Editor
OpenGeode (SDL)
MSC Editor
SOIS EDS Tool
OpenGeode (SDL)
SCM
Matlab / Simulink

## Slide 19: IXV Use Case
MODELLING DESCRIPTION

## Slide 20: Migration to GR740 and HAIR
Thesis
From TASTE generated source code skeletons an analysis was made of required change to executing in multi-core and TSP.
Demonstrated running in N2X and HAIR
7 partitions evenly distributed in time and in the four processor cores.

## Slide 21
ESROCOS
GR740 WITH

## Slide 22
EUROPEAN SPACE ROBOTICS CONTROL AND OPERATING SYSTEM (ESROCOS)
COMPET-04-2016. Proposal 730080

## Slide 23: ESROCOS Toolchain
OBJECTIVES
IMA Mixed-criticality (AIR)
Logging
Laboratory quality level (Linux)
High-reliability quality level
Space quality level (RTEMS)
PUS Services (TM/TC)
State-machines
for FDIR
ASN-1
Data types
Deployment, Configuration and Continuous Integration
Middleware (TASTE – PolyORB-HI/C)
Basic robotics libraries
Robotics Modelling
Third-party Open Source Robotics SW, Monitoring, Visualization, Simulation, Scripting
Real-Time SW Modelling and Analysis

## Slide 24: USE CASES
Results

## Slide 25
COMRADE
GR740 WITH

## Slide 26: Better SIL to PIL Transition
OBJECTIVES
  Upgraded SIL simulator to address critical aspects in early phases.
    GNC software.
    LEON4 processor.
  Include a software emulator of the target processor that lead significant improvements over SIL, yet simpler than PIL.
  Resulting V&V chain.
    MIL  Automatic Coding  SIL x86  SIL SPARC/LEON4  PIL  HIL

## Slide 27: Improved LEON4 Processor Emulator
Results
  ESOC Emulator Suite (ESOC EMU) selected for providing software emulation functionality with GMV’s LEON4 emulator from ESA HAIR project has been ported and enhanced for this activity.
  Designed to run a standalone process, launched from S-Function block.
  Software executed directly from code generated from Simulink.
  Pipes communications library with a client/server architecture also developed as part of this activity.

## Slide 28: Validation and Performance
CONCLUSIONS
  Inexpensive validation with representative tools, i.e., processor emulator, is beneficial for early error discovery.
  Development of SIL representative simulators in COMRADE has proven beneficial to assess the generated code early, and to mitigate risks during the ongoing PIL and HIL test campaigns.
Simulator | Base Frequency | Min. / Max. cycle count | Avg. Processor Free | WC Processor Free
eDeorbit Synchronisation | 30 Hz | 6062 / 1760962 | 94.34801715 % | 78.868456 %
eDeorbit Stabilisation | 30 Hz | 18755 / 2808688 | 86.2383149 % | 66.295744 %
ASSIST Synchronisation | 30 Hz | 6062 / 1605304 | 94.03503456 % | 80.736352 %
Notes: In summary, this upgraded SIL simulator is an affordable tool to mitigate risks and early performance assessment.

## Slide 29
MORA-TSP
Conclusion

## Slide 30: END TO END DEMONSTRATION
OBJECTIVES
  ESA Invitation to Tender AO/1-8834/17/NL/FE:
  “Multicore Implementation Of The On-Board Software Reference Architecture with TSP Capability”
  Multicore Implementation of the OBSW Reference Architecture with Time and Space Partioning
  Duration: 14 months
  Consortium:

## Slide 31: EAGLEEYE USE CASE MODEL
RESULTS

## Slide 32
EagleEye
Current Results
Page 32
TASTE has been upgrade to have AIR integrated and provide binaries running in TSP and SMP multicore.
Several EagleEye scheduling scenario have been drawn including partitions running in multiple cores with RTEMS 5 SMP.

## Slide 33
www.gmv.com
THANK YOU
daniel.silveira@gmv.com
lasg@gmv.com